## Slide 1
RETRO TV
PROJECT
By Haidar Ali Alshowaikh | Class 8E

## Slide 2
WHAT IT'S BUILT FROM
Materials Used
Replacement Pi 4
Arduino Uno
Volume knob
Speakers
Power button
Joystick Module
22-inch HDMI monitor
Enclosure frame
02
U

## Slide 3
SECTION 01 · THE IDEA
The Monitor...
I reused an available monitor and built a new TV experience around it, with joystick controls and a retro-style cabinet.
05

## Slide 4
SECTION 02 · THE PROBLEMS
Challenges That Took Work
INPUT
Making joystick navigation reliable on the Raspberry Pi
AUDIO
Routing sound to the right output and linking the knob to system volume
DISPLAY
Moving from the old laptop-panel setup to a 22-inch HDMI monitor
08

## Slide 5
SECTION 03 · SOLUTIONS
How I Fixed Them
System Volume
The knob changes system volume with wpctl; the OSD shows speaker percentage and mute.
Audio Output
mpv uses PipeWire and follows the Pi’s selected audio output.
Key Detection
Matches the joystick’s hardware keycode so TV-app controls respond reliably.
12

## Slide 6
SECTION 03 · SOLUTIONS
Current Status
The replacement Pi 4 boots to desktop. The merged update adds stream read ahead and smoother player cleanup; playback still needs testing on the Pi.
14

## Slide 7
SECTION 04 · THE WIRING
How A Button Press Travels
1. ARDUINO
Reads the joystick, knob, and button; sends a command over serial
→
2. THE BRIDGE
rpi_bridge.py turns that command into a real key or mouse event
→
3. THE APP
tv.py receives it like normal keyboard input and reacts on screen
17
U

## Slide 8
SECTION 04 · THE WIRING
Current Wiring Reference
 | PART | CONNECTION | PURPOSE
ARDUINO UNO | Joystick X/Y + click | Volume encoder A/B | USB serial to Pi
RASPBERRY PI | USB from Uno | HDMI to monitor | GPIO3 + GND to button
MONITOR | HDMI input | No LVDS connection | Monitor's own power
POWER BUTTON | Shutdown switch | GPIO3 + GND | Requests safe shutdown
POWER | USB-C to Pi | Monitor power cable | Uno powered over USB
21

## Slide 9
SECTION 04 · THE WIRING
Build and Test Flow
STEP 1
Connect joystick and encoder to the Uno
→
STEP 2
Flash the Uno and test USB commands
→
STEP 3
Set up the TV app and USB bridge on Pi
→
STEP 4
Connect HDMI monitor and test GPIO3 button
22

## Slide 10
SECTION 05 · GOALS
Goals
GOAL 1
Build a retro TV prototype with joystick-led control
GOAL 2
Build a customer-sized cabinet around the chosen monitor
24

## Slide 11
SECTION 06 · Programing
Hardware VS. Software
27
V S
Hardware
Software
Rassperi Pi
Arduino UNO
Python
C++

## Slide 12
THANKS!
Haidar Ali Alshowaikh | Class 8E